## Slide 1: Chase lab data pipeline
Hiroo Miyata

## Slide 2
Sorting
Connect to chase lab data server
By WinSCP
Download files
delayedCOut.plx or nev/
TaskData folder/ ns4 data
Export .nex file
Do check off export unsorted spike timestamps. Do not check any of the others
Import .nev file
Change directory to Rocky/XXXXAdam_2022/Blackrock_anterior/
Save sorted data into .plx
Export .plx file
Spike sorting
Sorting Techniques
まず、peak-valley vs PC2 をみる。二つ頭の形だったらまず間違いなくneuronが存在する。各場所ごとのwaveformを確認して、spikeっぽいところをadd unitする
PC2, PC1も明らかに分離していることが多いので、PC2 vs PC1も必ず見ること
そして時々PC3に重要なNeuron が隠れていることもあるので、PC3 vs PC2も必ず見ること
次に、境界線はどこら辺かを調べるのが大事。最初は細かくadd unitを行い、それらのcross correlationを確認する。その形から、どの神経集団が同じクラスターに存在するのか大体検討がつく。
次に、ノイズデータの除去をする。ISI=0にノイズデータがあった場合、PC1vsPC2でノイズの中心に近い神経データを除去する。スパイクの形に応じてPeak vs PC1 or PC2 もしくはValley vs PC1 or PC2を確認し、下限値を削除してあげると解決することがある。この時、事前にかく場所のwaveformを確認して、自分のremove wfが妥当かどうかを確認しておいたほうがいい。
最後に、Timestampを見る癖をつけたほうがいい。神経が動いたことにより取れる神経データが変化していないか、確認するべし。時々すごい変化して最初と最後で別のスパイクに見えることがあるので、TimeStampは要注意
大体スパイクが15000あると安心10000以下は基本ダメ
Unitの順序はそろえる。そうすることで後で見やすくなる
Export .txt file
Export Per-Unit Data/All Channels into one file/export fields are Channel and Unit Number/“Append Template Waveform Data in units of” and not “Template Std Dev Data”

## Slide 3
After sorting
zzz_synchRockyDataToTask
Make synchInterim data
wrapper_preprocessTaskAndKinematicData_choking
Make synchronized data
RockyDataPreprocessing
Make preprocessed datas
CombineTrialData
Make own dataset based on ones interest
Find bad trials
(fullTrialSpikeRateMat) < minSpikeRate
remove "outlier trials“
Template
pp_spikeAlignmentToTrial
Find bad units
mean(fullTrialSpikeRateMat,2) < minSpikeRate;
lowVarUnits = std(fullTrialSpikeRateMat,[],2) < minSpikeRate
Remove >75% increase or drop in FR
the channel just goes crazy and gets ridiculously high values
Remove duplicated "cross-talk" units

## Slide 4
Unit Identification
convert dataset each day to dataset across day
Check max FR difference allowed
Template
Convert data format from Chase Lab’s to Batista Lab’s
UnitDScriptForHiroo.m
Calculate mean firing rate, spike train, mean waveform
unitIdentification.m
Calculate correlations, wavescore, autoscore, basescore.
CorrScore : cross-correlograms between this neuron and every other neuron
Wavescore : The correlation of normalized
Autoscore : Inter-spike-interval (ISI) autocorrelation
Basescore : Daily change of log( length(spiketimes) / {max(FR) –min(FR)} )
Calculate survival and corrscore.
Find same channel and unit data,
Get corrscore : computeCorrScore
Update survival by 10 times computeSurvival
Calculate survival
Use wavescore, autoscore, basescore, corrscore
Get possibility if the units are the same
Update survival based on threshold (99%)
IterateSurvival.m
ComputeSurvival.m
Change the unitID to root unitID
p2_v3_unitIdentification_withSkips.m
p2b_chronicUnitTCs.m
Get the direction label and the spike train
in each trials and each unique units

## Slide 5
Get the following 4 statistics for each unit on each day:
Mean firing rate
Mean waveform snippet shape
Inter-spike-interval (ISI) autocorrelation (over like 100ms or something)
(Average? idr) inter-spike-interval cross correlation w/ all other units
So now for each unit on day 1 and day 2, you have 4-value vector that represents the "characteristics" of the unit
Create a null distribution of units that are certainly different
We know (biologically) units showing up on different electrodes on Utah arrays are not the same unit
So, you make a null distribution from the pairwise comparisons of units across different channels (and different days; e.g. Day1Chan1Unit1 vs. D1C2U1, vs. D1C2U2, vs. D1C3U1... vs D2C1U1... etc)
For the distribution, the features are, for each pair of units:
Mean FR score: The difference in log of the mean firing rates
Wave score: The (potentially shifted) correlation between the mean waveform shapes
Autocorr score: The correlation between autocorrelation shapes
XCorr score: Average correlation between cross-corellograms
These are all fisher tranformed (0 to 1 scale transform to gaussian distribution) to make them more gaussian
The most informative features tend to be Wave score and xcorr score tend to be the most informative
This 4D distribution of not same units tends to be very Gaussian and have very many points
Then, you get the same 4 features for each pair of potentially same units. So anything on the same channel (i.e., D1C1U1 vs. D2C1U1, D2C1U2)
Units that are different across days tend to fall into the null distribution, whereas ones that are the same across days form a new gaussian cluster in the 4D space
So basically you have a ton of points (null) labeled as "not same" and some labeled as "not sure"
Fit a gaussian mixture model (k = 2) with one gaussian initialized as the null distribution and I think the other as the mean/cov of the not-sure distribution (which then quickly settles out to the actually-the-same-unit distribution after a few iterations)
To select a decision boundary, they use a 5% false discovery rate
i.e., make the same-unit Gaussian big enough to capture ~5% of the opposite class as well
If we have enough units, I like to use 1% instead, but do whatever you feel